## Slide 1
Research framework: How greenway landscape characteristics affect visual-thermal perception in Guangzhou, China
Core contribution: an integrated workflow linking image analytics, field measurement, VR validation,
controlled experimentation, and perception-coupling analysis for climate-adaptive greenway design.
Step 1: Greenway image database construction and type identification
1
Study area and data acquisition
Guangzhou greenway network
OSM official greenway
planning data
Baidu street view sampling
every 50 m
8,428 images collected;
2,994 valid panoramic images
...
2
Semantic segmentation of greenway scenes
DeepLab v3+
ADE20K dataset
Quantification of visual elements
Sky
Trees
Road
Buildings
Water
Other
3
Greenway typology and prototype selection
Urban greenways
Community leisure
Roadside
Countryside greenways
Open
Waterfront forest
Mountain exploration
Community leisure greenway
selected as the VR prototype
Step 2: Construction of visual-thermal landscape feature indicators
1
Candidate factor extraction
19 candidate
landscape
factors
Derived from
semantic results
Derived from
literature
Derived from linear
greenway characteristics
2
Questionnaire screening and dimension reduction
306 valid
questionnaires
Reliability
analysis
Principal component
analysis(PCA)
3
Expert confirmation and final indicator system
Interview and
UAV-video-assisted review
17 experts/students
consulted
Final 7 dimensions and 10 key factors
Environmental
naturalness
Water
visibility
Plant color
richness
Plant
morphology
Plant
density
Road material
naturalness
Surrounding
environment type
Sky
shading
Sky
condition
Greenway
curvature
Step 3: Field validation and VR-climate chamber experiment
1
Outdoor field measurements
3 typical scenes on a
campus community greenway
Microclimate: Ta, RH, Va,
Tg.MRT
Subjective survey
physiological measurements
40 participants
2
VR platform feasibility validation
1:1 scene reconstruction
with MARS2020
Immersive display by
HTC VIVE
Compare real vs.
virtual environment
Consistency results
Temperature difference
< 0.5 °C
Humidity difference < 2%
Blood pressure difference
< 4 mmHg
Most subjective vote
differences 8%
3
Controlled VR experiment under thermal conditions
Pretest based on 12 monthly
typical meteorological days
3 thermal conditions:
cold(December),
hot(June), moderate(August)
11 standardized VR scenes:
1 base scene+ 10 single-
factor scenarios
83 participants,
randomized into
3 groups
30 min adaptation+
5 min observation
per scene
Step 4: Coupling analysis and design implication extraction
1
Statistical analysis
Pearson correlation analysis
Multiple linear regression
Comparison across thermal
conditions and scenarios
2
Mechanism identification
Coupling between perception and satisfaction
Visual
perception
Thermal
perception
Overall
satisfaction
Overall satisfaction 0.659 × visual satisfaction + 0.344 × thermal satisfaction
3
Key findings and design outputs
Water visibility is the most influential
cross-dimensional factor
Important factors: environmental
naturalness, road material naturalness,
greenway curvature, sky shading,
plant density
Output: evidence for visual-thermal
integrated greenway design and
climate-adaptive planning in hot-humid cities